## Slide 1: Power Study
IMU, Temp Sensor, 16% Duty Cycle
Transmitter: ~1% Duty Cycle
Timing:
Boot + 1 Transmit
Loop:
  Sleep for 10 Seconds
  Boot IMU+Env Sensor for 2 Seconds
  Sleep for 10 Second
  Goto Loop
LOW POWERED MCU

## Slide 2: Small View
Transmit
IMU On
IMU Sleep

## Slide 3: Super Small View
Energy ~=
0.1571 J
(From Integration under Power Curve)
Cap_E = ½*C*V^2
C = 2* Cap_E/(V^2)
Required Capacitance =
0.3142 F

## Slide 4: Medium View

## Slide 5: Big View: ~8 mins of Data

## Slide 6
Transmission 50%
Timing:
Boot
IMU to Off
Loop:
  Boot LoRa for 3 Seconds (~1 Transmission)
  Sleep for 3 Second
  Goto Loop
HIGH POWERED MCU
- The high powered MCU was put on by accident and consumes more transmission power than the low powered MCU by approximately 50%.
LoRa Power Study
High Powered
Low Powered

## Slide 7: Single Transmission
Energy ~=
0.06 J
(From Integration under Power Curve)
Cap_E = ½*C*V^2
C = 2* Cap_E/(V^2)
Required Capacitance =
0.12 F
Brown out from voltage regulator
(BO)

## Slide 8: Sleep to Transmission to Sleep
Energy ~=
0.281 J
(From Integration under Power Curve)
Cap_E = ½*C*V^2
C = 2* Cap_E/(V^2)
Required Capacitance =
0.5620 F
(BO)

## Slide 9: Medium View

## Slide 10: Large View (~5 min of data)
Accidently hit the power off button on the power supply

## Slide 11: Total E for each Event
Processor
Processor+IMU
Processor+Transmitter
Put Temp Sensor to Sleep